## Slide 1
Analysis of Stress Concentration in cylindrical body having a cavity
Presented by:
Nikhil Dewangan
(Self project)

## Slide 2: CONTENTS
    Problem Statement
    Solution
    FEM Process
    Comparison
    Conclusion
    References

## Slide 3: Problem Statement
A cylindrical solid with of height (h) and diameter (w=0.5 h) with an axisymmetric ellipsoidal cavity having major and minor axis of 2a and 2b lengths, respectively, at the center of the cylinder. a = 0.1w.
Consider b = a, a/2, a/6, a/10.
Compare stress concentration and stress distribution along line AB for different cases.

## Slide 4: Solution
Consider
Hight (h) = 100mm
Diameter(W ) = 0.5*h = 50mm
Major axis length (a) = 0.1W = 5mm
Young's modulus (E) = 206 GPa
Nominal stress () = E ɛ = 41.2 MPa
Cases | Condition | Stress concentration factor
A | a / b = 1 | 2.046
B | a / b = 2 | 3.313
C | a / b = 6 | 11.817 ( by linear interpolation between Case B and D)
D | a / b = 10 | 13.52

## Slide 5: Creation of Part

## Slide 6: Assigning material properties & Boundary Condition

## Slide 7: Meshing

## Slide 8: Result in case A (b = a)
Stress at point A = 84.547 MPa
Stress at point B = 40.752 MPa
SCF (K) = 2.0521

## Slide 9: Result in case B (b = a/2)
Stress at point A = 136.076 MPa
Stress at point B = 40.901 MPa
SCF (K) = 3.3028

## Slide 10: Result in Case C (b = a/6)
Stress at point A = 291.654 MPa
Stress at point B = 41.0425 MPa
SCF (K) = 7.0789

## Slide 11: Result in Case D (b = a/10)
Stress at point A = 428.19 MPa
Stress at point B = 41.074 MPa
SCF (K) = 10.3929

## Slide 12: Graph of all cases
Case A
case B
case C
Case D

## Slide 13: Combine graph
Stress in MPa
Normalized distance
Chart: 

## Slide 14: Comparison
Sr. No | Cases | SCF by FEM | Actual SCF | Error in %
A | b = a | 2.0521 | 2.045 | 0.3471
B | b = a / 2 | 3.3028 | 3.313 | 0.3078
C | b = a / 6 | 7.0789 | 11.817 | 40.09
D | b = a / 10 | 10.3929 | 13.520 | 23.12

## Slide 15: For Poisson’s ratio is 0.498
Case B
Case A
Case C
Case D

## Slide 16: Conclusion
SCF increases with decrease in ratio of b/a
SCF is minimum when ratio of b/a is 1

## Slide 17: References
Theory of elasticity and stress concentration by Yukitaka Murakami

## Slide 18
Thank you